## Slide 1: Mobility aware and energy-efficient federated deep reinforcement learning assisted resource allocation for 5G-RAN slicing
Yaser Azimi, Saleh Yousefi, Hashem Kalbkhani, Thomas Kunz
Computer Communications - Jan 2024
Presenter- Divya K.

## Slide 2: Abstract
Allocation of power and radio block (RB) resources in a multi-RAN scenario
Users of both rate-based and resource-based slices are considered
Mobility-aware and energy-efficient federated deep reinforcement learning-assisted resources allocation (ME-FDRL-RA) solutions are proposed
Deep learning models considered:
  Stacked and bidirectional long-short-term memory (SBiLSTM)
  Allocate resources to slices on a large timescale
  Federated advantage actor-critic (F-A2C) allocates resources to a small time-scale
For RA, iterative algorithm – Interference-aware and energy-efficient power allocation (IA-EPA)
MF-FDRL-RA: Parameters – convergence speed, computational complexity, energy efficiency, number of accepted users
  Challenges – User mobility, maintaining degree of inter-slice isolation

## Slide 3: Introduction
Distributed architecture – RRUs + Dus + CU
Architectures proposed –
  D-RAN
  C-RA
  O-RAN
  F-RAN
  v-RAN

## Slide 4: System Model
Assumptions – RANs have identical no.of slices and computational resources
Distributed RAN with O-RAN architecture where DU and CU are centralized in BBU
DU responsible for running RA algorithms
DU controllers communicate via orchestrator layer
CU runs aggregator using obtained data from agents to increase convergence speed

## Slide 5: System Model
Fixed users and mobile users
Mobile users' movement model based on SWIM
Weight of destination cell C from home cell A –

## Slide 6: Problem definition and formulation of RA
Problem 1 – Resource Slicing with Mobility Awareness on a Large Time-Scale
  Mobile and fixed users’ traffic – predict required resources for next PW
  Meet QoS requirements
  Minimize the error - MSE

## Slide 7: Problem definition and formulation of RA
Problem 2 – Resource Allocation to Users Per Slice on a Small Time-Scale
  Online resource allocation
  Control unpredicted traffic changes on large time-scale
  Difference between amount of allocated resources before and after resource reconfiguration per slice –
  Problem formulated -

## Slide 8: Problem definition and formulation of RA
Problem 3 – Determining the Required Resources for Users of Slices
  Users’ resources in rate-based slice
  Increase energy efficiency, spectrum efficiency, improve QoS of users
  Considering channel conditions such as inter-RAN interference and user mobility

## Slide 9: Proposed Solutions
ME-FDRL-RA components –

## Slide 10: Proposed Solutions
ME-FDRL-RA components –
  DU-Controllers: Runs DRL, SBiLSTM, IA-EPA algorithms, assigns power and radio resources
  Orchestrator: exchange information (CSI and user Mobility)
  Parallel F-A2Cs for set of slices per RAN: each RAN slice represents an F-A2c agent
  Shared account book for each RAN: each RAN shares info related to current PW and previous PW to estimate allocated resources for next PW
  IA-EPA method: iterative method to find optimal answer by considering the channel conditions and energy efficiency
  SBiLSTM model for each slice in each RAN: to guarantee isolation among slices
  Global Aggregator for F-A2Cs: to increase the convergence speed and improve F-A2C agents' decisions

## Slide 11: Proposed Solutions
Large time-scale prediction
  Track total traffic of fixed and mobile users in each time step
  Sum of required resources for fixed users and mobile users of slice m in RAN b – input data for the prediction of allocated resources in slice m of Ran b in next PW
  Confidence intervals, sample mean, and standard deviation of predicted values is calculated
  Dynamically tuned during simulation
  Upper bound for confidence interval is applied

## Slide 12: Proposed Solutions
Interference Aware and Energy-efficient Power Allocation (IA-EPA)
  Gradient-descent-based sub-optimal method
  Trade-off between the achievable rate and power consumption while considering interference caused by other transmitters
  2 subproblems –
    Minimum no.of idle RB
    Minimum amount of power to maximize energy efficiency

## Slide 13: Proposed Solutions
Samll time-scale prediction
  Uses F-A2C for RA on small time-scale for each slice
  Model –
  Each slice makes the decision on RA
  Accept/Reject new user is independent to other slices

## Slide 14: Proposed Solutions
Scalability Assessment and Signaling Overhead
  Each RAN is managed by a DU
  Each DU-Controller executes RA algorithm, includes F-A2C agents, IE-EPA methods, SBiLSTM models for each RAN
  Each Slice has 2 F-A2C agent, IA-EPA method, SBiLSTM model
  Deployment scenarios:
    Case 1 – Single system/multiple threads
    Case 2 – Multiple systems/multiple threads
    Case 3 – single system/single thread

## Slide 15: Simulation results
Multi-Ran: 4 RANs
Slice m of RAN b arrival and departure rates: 𝜆[𝑚, 𝑏] and 𝜇[𝑚, 𝑏].
Requests assigned by FIFO policy
Fixed total number of users for mobility model
In F-A2C, rejection penalty is twice as isolation violation penalty
10 slices of RAN: 4 – resource-based, 6 – rate-based
FDRL uses 4 agents
Simulation includes 48000 time steps, PW – 1200 time steps
Each RAN has 200 users

## Slide 16: Simulation results

## Slide 17: Simulation results
Competitive methods –
  Extended EE-DRL-RA
  Extended iRSS
  E-FDRL-RA
  ME-DRL-RA
  Static Method

## Slide 18: Simulation results
Traffic prediction accuracy for SBiLSTM model on a large time-scale

## Slide 19: Simulation results
Convergence speed for the compared methods in the multi-RAN scenario.

## Slide 20: Simulation results
Energy efficiency versus number of iterations with different transmission rates in IA-EPA method.

## Slide 21: Simulation results
(a) Total energy efficiency (b) Average user acceptance percentage

## Slide 22: Simulation results
(a) Utilization of slices (b) Isolation degree among slices

## Slide 23: Simulation results
The effect of confidence level on isolation degree in a large time-scale.

## Slide 24: Simulation results
The effect of SWIM mobility degree in ME-FDRL-RA.
The effect of the number of human mobile users in ME-FDRL-RA