## Slide 1: Introduction to Routing and Spectrum Allocation (RSA) in Optical Networks
Divya K

## Slide 2: Welcome and Overview
What is Routing and Spectrum Allocation (RSA)?
Learning Objectives:
  Understand the concept of RSA
  Know the key components of optical networks
  Learn how routing and spectrum decisions are made

## Slide 3: What is an Optical Network?
A network is a collection of connected devices that exchange data
In optical networks, data travels as light through fiber cables

## Slide 4: What is an Optical Network?
Components:
  Nodes (routers/switches)
  Links (fiber cables)
  Spectrum (set of frequency slots)
  Source: The starting point of the data
  Destination: Where the data is going
B
A
D
E
F
C
Src
Dest
Notes: Explain frequency slots using the traffic and lanes example

## Slide 5: How to Find the Shortest Route
The shortest route = the path with the least distance or hops
  Given Example: By hop count
  shortest path: A – B – C – F or A – D – E – F
Algorithm used: Dijkstra’s Algorithm
  By the least distance
  Shortest path: A – B – D – E – F
B
A
D
E
F
C
Src
Dest
4
11
5
3
9
13
6
2

## Slide 6: The RSA Problem Defined
Goal: Find a path (route) and assign spectrum slots
Must avoid interference and ensure availability
Constraints:
  Spectrum continuity (same slot used on every link in the path)
  Spectrum contiguity (slots must be next to each other)
  Non-overlapping spectrum assignment (no reuse on the same link)

## Slide 7: Understanding Routing
Routing = Selecting a path from source to destination
A path is made of a sequence of links (like roads between cities)
Considerations:
  Network layout (topology)
  Which links are available
B
A
D
E
F
C
Src
Dest
4
11
5
3
9
13
6
2

## Slide 8: Understanding Spectrum Allocation
Each link has a number of frequency slots (like lanes on a road)
Goal: Assign a group of slots that are:
  Available on all links of the path
  Next to each other (contiguous)
Why it matters:
  Avoid signal interference
  Make efficient use of the network

## Slide 9: Understanding Spectrum Allocation
Constraints
  Continuity
  Contiguity
  Non-overlapping

## Slide 10: RSA Example
Spectrum slot req – 3
A – B – C – E – F : Slots 4, 5, 6
B
A
D
E
F
C
Src
Dest

## Slide 11: Why RSA is Important
Without RSA:
  Data could get delayed or blocked
  The network could waste bandwidth
With RSA:
  Better use of available resources
  Faster and more reliable communication

## Slide 12: Summary and Questions
Routing: Choosing a path
Spectrum Allocation: Choosing frequency slots
RSA helps make networks faster and more efficient
Any questions?

## Slide 13: resources
https://www.researchgate.net/publication/307873989_Study_and_Analysis_of_Routing_and_Spectrum_Allocation_RSA_and_Routing_Modulation_and_Spectrum_Allocation_RMSA_Algorithms_in_Elastic_Optical_Networks_EONS
https://www.youtube.com/watch?v=gQtgtKtvRdo&ab_channel=SabinCivilEngineering
https://www.youtube.com/watch?v=Cwv54dV-a7s&ab_channel=LeslieRusch